## Slide 1: SOC Center of Excellence Device Trees for Intel SoC FPGAs Dan Negvesky November 2016

## Slide 2: Agenda
Background
Device Tree Overview
  Hierarchy
  Loading a device tree
  Drivers and bindings
  Examples
FPGA Regions & Device Tree Overlays
Creating a Device Tree
  Examples
Appendix – fully annotate device tree example

## Slide 3: Background
Before device trees…
  Non-discoverable hardware (e.g. I2C, SPI, UART, Ethernet controllers, etc.) as part of an embedded system was described using C code compiled directly in the kernel (uImage or zImage).
  Bootloader passed additional information to the kernel and a machine type integer identified the board.
Use of device trees with ARM began in 2011 (predating the release of Altera SoC).
With device trees…
  Hardware description is located in a separate binary called the device tree blob or device tree binary (.dtb)
  Bootloader loads the kernel (uImage or zImage) and the device tree binary (.dtb)

## Slide 4: What is a Device Tree?
Device trees use a hardware description language to describe the hardware available to an embedded system (e.g. Altera SoCs)
This typically consists of non-discoverable hardware, non-discoverable buses (e.g. I2C, SPI), and external hardware attached to them (e.g. LCD display).
They consist of a tree data structure of nodes, with each node having properties (address, interrupt, driver info) that describe the device.
Device tree source (.dts) files are compiled into a device tree blob (.dtb), either during kernel build or separately, using a device tree compiler (DTC).
Can be used by the bootloader (Arria 10) or the kernel.
Can be flat or hierarchical.
Device trees are kernel version dependent (e.g. your 3.10-ltsi kernel .dtb will not work with the 4.1.22-ltsi kernel).

## Slide 5: Device Tree Usage
Static
  Base (board level) device tree defines all external hardware, HPS and FPGA peripherals used by the specific embedded system
  The boot loader is responsible for loading the kernel image (zImage used for socfpga) and device tree blob (.dtb) into memory.
Dynamic
  Base (board level) device tree defines external hardware, HPS, and “FPGA Regions”
  Device tree overlay defines FPGA peripherals to be added, or overlayed, to FPGA Region in live device tree
  Device tree overlay file (.dtso) gets compiled and added to the root filesystem
  Boot loader loads board level tree, then after FPGA configuration (optional), overlay gets appended to main tree by an init script
  Applying the overlay can also (re)configure the FPGA if specified in the overlay
Notes: FPGA can be configured prior to loading overlay, or loading the overlay can trigger FPGA configuration

## Slide 6: Creating a device tree (1/2)
Old method
  Kernel 3.10-ltsi examples on rocketboards.org
    Used the sopc2dts tool (originally developed for Nios) to read .sopcinfo board and system .xml files and automatically output .dts/.dtb files
    Creates a flattened device tree
    Still requires the user to manually edit/create/customize a board level .xml file
    See Device Tree Generator User Guide (v15.1)
Notes: Since the introduction of Altera (now Intel) SoCs, the adopted flow for creating a device tree was to use the sopc2dts tool (originally created for generating device trees for Linux on Nios).
Inputs to sopc2dts:
.socpinfo file from Qsys
board .xml file (user created)
system .xml file (user created)

## Slide 7: Creating a device tree (2/2)
Newer method
  sopc2dts tool does not generate functional device trees for the newer kernels, specifically the latest ltsi kernel (currently 4.1.22)
  sopc2dts still partially usable to extract the FPGA peripherals
  sopc2dts may be updated in the future to produce usable device trees again - overlay
  For kernel 4.1.22-ltsi
    Use example hierarchical device trees that are part of the kernel source located in /arch/arm/boot/dts.
    See full example in Appendix.
    From Device Tree Generator User Guide :
Warning: The Linux Device Tree Generator is tested with and supports only the Linux kernel version targeted by the associated GSRD. For the 15.1 GSRD release this 3.1-ltsi. It is not recommended to use the Linux Device Tree Generator if your design targets a different Linux kernel version. It is instead recommended to manage the Device Tree manually in such a case, using the Device Tree files provided by the kernel as a baseline, and adding the FPGA IP and board information manually.
Notes: This is whole the reason to understand Device Tree syntax.
Without the automated tool to generate, you need to understand how to create your own.
Board level device tree replaces board level .xml file used by sopc2dts. Why use .xml when you can directly modify the .dts? Format is more readable than .xml.

## Slide 8: Device tree hierarchy (1/2)
Device trees created by sopc2dts are flattened device trees (i.e. most examples on rocketboards for 3.10-ltsi kernel).
Newer kernels use hierarchical device tree structure.
Each board should have its own device tree.
Different boards that use the same processor (e.g. Intel/Altera SoC devices that use the same hard processor subsystem, or HPS), can include other device trees that define common features.
  Located in kernel tree arch/arm/boot/dts
    socfpga.dtsi
    socfpga_cyclone5.dtsi
    socfpga_arria5.dtsi
    socfpga_arria10.dtsi
Use #include in board level device tree to “layer” multiple trees.
Notes: See example next slide.

## Slide 9: Device tree hierarchy (2/2)
.
.
.
.
.
#include "socfpga_cyclone5.dtsi"
/ {
model = "Terasic SoCkit";
compatible = "altr,socfpga-cyclone5", "altr,socfpga";
.
.
.
Board device tree socfpga_cyclone5_sockit.dts
.
.
.
.
/dts-v1/;
/* First 4KB has trampoline code for secondary cores. */
/memreserve/ 0x00000000 0x0001000;
#include "socfpga.dtsi"
/ {
soc {
clkmgr@ffd04000 {
clocks {
.
.
.
Cyclone V common device tree socfpga_cyclone5.dtsi
.
.
.
.
#include "skeleton.dtsi"
#include <dt-bindings/reset/altr,rst-mgr.h>
/ {
#address-cells = <1>;
#size-cells = <1>;
aliases {
ethernet0 = &gmac0;
ethernet1 = &gmac1;
serial0 = &uart0;
.
.
.
socfpga common device tree
socfpga.dtsi
/*
* Skeleton device tree; the bare minimum needed to boot; just
* include and add a compatible value. The bootloader will
* typically populate the memory node.
*/
/ {
#address-cells = <1>;
#size-cells = <1>;
chosen { };
aliases { };
memory { device_type = "memory"; reg = <0 0>; };
};
Bare minimum skeleton.dtsi
Compiled socfpga_cyclone5_sockit.dtb
(binary device tree blob)
Notes: Example using Arrow SoCKit device tree from kernel source
All of these example device trees come from arch/arm/boot/dts from the socfpga-4.1.22-ltsi branch
The Cyclone 5 SoC Development Kit device tree uses a #include to layer in socfpga_cyclone5.dtsi, which then #includes socfpga.dtsi, which #includes skeleton.dtsi.
The output of the device tree compiler includes all of these layers into the binary device tree blob (.dtb)
Compiler can also be used to create a flattened .dts (can be useful for debugging problems)

## Slide 10: Device trees, drivers, and bindings (1/3)
In a device tree source node entry, the compatible string and various properties are used to bind a device to its corresponding driver.
In the device driver source, the of_match_table field of the struct device_driver lists the compatible strings supported by the driver.
In the device tree binding, the required and optional properties and values of the device tree entry are defined to provide device attributes needed for the driver.
  Device Tree bindings are documented in kernel source tree in Documents/devicetree/bindings
  New bindings reviewed by Device Tree maintainers by sending to devicetree@vger.kernel.org.
Notes: This discusses how a driver is connected with an entry in the device tree
See example next slide

## Slide 11: Device trees, drivers, and bindings (2/3)
* TTY on a Newhaven NHD‐0216K3Z‐NSW‐BBW LCD connected to I2C
Required properties:
- compatible: Should be "newhaven,nhd‐0216k3z‐nsw‐bbw";
- reg: i2c address
- height: should be 2 lines
- width: should be 16 characters
- brightness: backlight brightness. Range is 1 to 8, where
1=OFF and 8=maximum brightness.
Example:
&i2c0 {
lcd: lcd@28 {
compatible = "newhaven,nhd‐0216k3z‐nsw‐bbw";
reg = <0x28>;
height = <2>;
width = <16>;
brightness = <8>;
};
device tree binding - newhaven_lcd.txt
&i2c0 {
status = "okay";
speed-mode = <0>;
/*
* adjust the falling times to decrease the i2c frequency to 50Khz
* because the LCD module does not work at the standard 100Khz
*/
i2c-sda-falling-time-ns = <5000>;
i2c-scl-falling-time-ns = <5000>;
lcd: lcd@28 {
    compatible = "newhaven,nhd-0216k3z-nsw-bbw";
reg = <0x28>;
eight = <2>;
width = <16>;
brightness = <8>;
};
board device tree - socfpga_cyclone5_socdk.dts
static const struct of_device_id lcd_of_match[] = {
{ .compatible = "newhaven,nhd-0216k3z-nsw-bbw", },
{},
};
static const struct i2c_device_id lcd_id[] = {
{ DRV_NAME, 0 },
{ }
};
MODULE_DEVICE_TABLE(i2c, lcd_id);
static struct i2c_driver lcd_i2c_driver = {
.driver = {
.name = DRV_NAME,
.owner = THIS_MODULE,
.of_match_table = lcd_of_match,
},
.probe = lcd_probe,
.remove = lcd_remove,
.id_table = lcd_id,
};
newhaven_lcd.c driver
1.
2.
3.
The i2c0 controller is defined in socfpga.dtsi and is referred to by &i2c0 in board level .dts file. It is enabled with status = “okay”
The device tree binding defines the required and optional properties and values that should be declared in the device tree. The lcd is defined as a child node of the parent i2c0 node.
A node in a device tree is bound to a driver by using the compatible string.
The of_match_table field of struct i2c_driver lists the compatible strings supported by the driver.
Newhaven LCD driver example
4.
phandle
2.
Notes: Example of external hardware on board (LCD character display) connected to a bus (I2C).
- The LDC is a child node under the i2c0 parent node, i.e. the I2C LCD controller is attached to I2C0 on the HPS

## Slide 12: Device trees, drivers, and bindings (3/3)
For the kernel to successfully load a driver (using a device tree)
  Device must be declared in the device tree
  Device tree properties defined correctly
    “compatible” string that identifies the driver
    Physical address allocated to the device
    Interrupts (if any) used by the device
Kernel scans “compatible” entries in device tree and matches with list of known drivers (compiled in kernel or loadable modules)
Notes: See example next slide
Most of the drivers in the kernel source tree (for ARM based device) are device tree oriented
Driver does NOT have to use a device tree – can be loaded without device tree
When writing a driver, you may our may not import parameters from a device tree

## Slide 13: Device Tree Entry – Example 1
i2c0: i2c@ffc04000 {
#address-cells = <1>;
#size-cells = <0>;
compatible = "snps,designware-i2c";
reg = <0xffc04000 0x1000>;
clocks = <&l4_sp_clk>;
interrupts = <0 158 0x4>;
status = "disabled";
};
node-name@unit-address: unit-address should match first address in reg property.
label – use phandle &i2c0 to refer to this node in other sections of the device tree or in board level device tree
This device is disabled at this level.
From HPS Memory Map
Property names and values
i2c0 entry from socfpga.dtsi
Interrupt type
Interrupt number
Level sense encoding
Device driver binding
This device is clocked by l4_sp_clk
Defines # of 32 bit address cells and # of 32 bit length cells used in a child node’s reg property.
Notes: socfpga.dtsi comes from kernel source arch/arm/boot/dts
socfpga.dtsi is common to Altera SoC Cortex-A9 families (Cyclone V, Arria V, Arria 10), so base address of i2c0 is common to all devices
For #address-cells and #size-cells, see previous Newhaven LCD example. Notice that reg property in LCD child node under i2c0 has 1 address field and no length field, corresponding to #address-cells = <1> and #size-cells = <0>
All of these entries are required

## Slide 14: Example 1 (cont’d) – interrupts (1/2)
i2c0: i2c@ffc04000 {
#address-cells = <1>;
#size-cells = <0>;
compatible = "snps,designware-i2c";
reg = <0xffc04000 0x1000>;
clocks = <&l4_sp_clk>;
interrupts = <0 158 0x4>;
status = "disabled";
};
Interrupt type:
0 = non-SPI
Non-zero = SPI
The ARM Cortex A9 TRM defines 3 interrupt types:
Software Generated Interrupt (SGI)
Private Peripheral Interrupt (PPI)
Shared Peripheral Interrupt (SPI)
Most will be non-SPI type.
For non-SPI type interrupts, take the GIC interrupt number and subtract 32:
190 - 32 = 158
For SPI interrupts, take interrupt number and subtract 16.
Interrupt number:
Refer to the Cyclone V SoC TRM, Generic Interrupt Controller, “GIC Interrupt Map” table.
Notes: HPS peripheral example: i2c0 (continuing from previous example).
Interrupts property explained:
First field is interrupt type. Most cases will be 0 (non-SPI).
Second field is interrupt number, translated by a function in the gic driver.
Translated Interrupt number = GIC Interrupt Number (from HPS TRM) – 32 (for non-SPI interrupt type, or -16 for SPI interrupt type.

## Slide 15: Example 1 (con’d) – interrupts (2/2)
i2c0: i2c@ffc04000 {
#address-cells = <1>;
#size-cells = <0>;
compatible = "snps,designware-i2c";
reg = <0xffc04000 0x1000>;
clocks = <&l4_sp_clk>;
interrupts = <0 158 0x4>;
status = "disabled";
};
Level sense encoding:
0x0 = “as already configured” (typically from boot loader)
0x1 = rising edge
0x2 = falling edge
0x4 = high
0x8 = low
Specifies drivers/i2c/busses/i2c-designware-platdrv.c driver, which #includes linux/interrupts.h
.
.
.
/*
* These correspond to the IORESOURCE_IRQ_* defines in
* linux/ioport.h to select the interrupt line behaviour. When
* requesting an interrupt without specifying a IRQF_TRIGGER, the
* setting should be assumed to be "as already configured", which
* may be as per machine or firmware initialisation.
*/
#define IRQF_TRIGGER_NONE 0x00000000
#define IRQF_TRIGGER_RISING 0x00000001
#define IRQF_TRIGGER_FALLING 0x00000002
#define IRQF_TRIGGER_HIGH 0x00000004
#define IRQF_TRIGGER_LOW 0x00000008
.
.
.
Notes: Last field is level sense encoding, defined in interrupts.h from linux source.
This is included in the i2c-designware driver referred to in the compatible property for i2c0.

## Slide 16: Example 2 – FPGA peripheral w/ interrupt
jtag_uart: serial@0x100020000 {
compatible = "altr,juart-15.1", "altr,juart-1.0";
reg = <0x00020000 0x00000008>;
interrupt-parent = <&intc>;
interrupts = <0 42 4>;
clocks = <&clk_0>;
};
For non-SPI type interrupts, take the GIC interrupt number and subtract 32:
42 = 74 - 32
Referring again to the Cyclone V SoC TRM, Generic Interrupt Controller, “GIC Interrupt Map” table.
There are 64 general purpose FPGA-to-HPS interrupts that allow soft IP in the FPGA to trigger interrupts in the MPU’s GIC.
• f2h_irq0 - FPGA-to-HPS interrupts 0 - 31
• f2h_irq1 - FPGA-to-HPS interrupts 32 - 63
phandle to interrupt-parent, defined in socfpga.dtsi, which
uses Cortex A9 GIC
IRQ 2
Notes: FPGA peripheral example: jtag_uart added in Qsys
Jtag_uart assigned to IRQ2, attached to f2h_irq0 on HPS.
This corresponds to GIC Interrupt Number 74 in the GIC Interrupt Map table.
Since this is a non-SPI interrupt (first interrupt field =0), subtract 32 to get translated interrupt number 42.
Last field indicates it will be level sensitive high trigger.
Also note that the interrupt-parent is &intc, which is defined in socfpga.dtsi and will using the arm,cortex-a9-gic driver as defined in the compatible property in this device tree entry.

## Slide 17: FPGA Regions Framework and Device Tree Overlays

## Slide 18: FPGA Regions Framework
FPGA Regions framework was introduced as a way to (re)configure an FPGA through an OS and allow any new hardware to be visible in the device tree (via overlay).
FPGA Region in device tree is the parent node to custom FPGA hardware modules added to Qsys system (i.e. hardware not part of the HPS)
  Can be defined in base (live) tree
  Can be added to by overlay
FPGA Region must include properties that add entries needed for configuration of the FPGA (FPGA Manager, FPGA Bridges)
Notes: Example will demonstrate this
FPGA Manager used for FPGA configuration
FPGA Bridges may need to be controlled during reconfiguration

## Slide 19: FPGA Region Device Tree Properties
Required properties
  compatible = "fpga-region";
  fpga-mgr : contains a phandle to an FPGA Manager (e.g. fpga-mgr = <&fpga_mgr>;)
  fpga-bridges : contains a list of phandles to FPGA bridges (e.g. fpga-bridges = <&fpga_bridge0>, <&fpga_bridge1>, <&fpga_bridge2>, <&fpga_bridge3>;)
  #address-cells, #size-cells : defines # of cells used to encode addresss and size cells of child node’s reg property
  ranges : defines child-bus-address, parent-bus-address, length
Properties added in overlay
  firmware-name : name of an FPGA configuration file in the firmware search path (described in firmware class documentation)
  partial-fpga-config : boolean, used with FPGA partial reconfiguration, used with firmware-name to specify configuration file
  external-fpga-config : boolean, used if FPGA is already configured
Notes: Example will demonstrate this next slide

## Slide 20: Example device tree FPGA Region entry
base_fpga_region: base-fpga-region { compatible = "fpga-region"; fpga-mgr = <&fpga_mgr>; fpga-bridges = <&fpga_bridge0>, <&fpga_bridge1>, <&fpga_bridge2>, <&fpga_bridge3>; #address-cells = <0x2>; #size-cells = <0x1>; ranges = <0x00000000 0x00000000 0xc0000000 0x20000000>, <0x00000001 0x00000000 0xff200000 0x00200000>;
};
Required properties for FPGA Region
Handles address space mapping for child nodes
Physical base address of FPGA slaves accessed via LWHPS2FPGA bridge
address span of LWHPS2FPGA bridge (1 cell)
fpga_bridge0: fpga_bridge@ff400000 {
compatible = "altr,socfpga-lwhps2fpga-bridge";
reg = <0xff400000 0x100000>;
resets = <&rst LWHPS2FPGA_RESET>;
reset-names = "lwhps2fpga";
clocks = <&l4_main_clk>;
};
These entries are found under the soc node in socfpga.dtsi
fpga_mgr: fpgamgr@ff706000 {
compatible = "altr,socfpga-fpga-mgr";
reg = <0xff706000 0x1000
0xffb90000 0x20>;
interrupts = <0 175 4>;
};
Virtual address mapping for device tree (2 cells)

## Slide 21: Device Tree Overlay Overview
Device tree overlays are used to add additional device nodes to a “live” tree currently loaded by the kernel.
  The live device tree could be a typical board level tree (using hierarchy) with minimal device entries.
  Live tree must contain FPGA Region, FPGA Manager, and FPGA Bridges (if they exist)
The target of the device tree overlay is the FPGA Region; all new nodes are inserted as child nodes here (typically /soc/base_fpga_region)
Overlay is applied in Linux by adding overlay .dtb to configfs (example to follow)
Overlays can allow the OS to (re)configure the FPGA
  FPGA configuration files (.rbf) added to /lib/firmware

## Slide 22: Why use Dynamic Device Tree Overlay?
FPGA hardware design changes
  May be easier to only have to update an overlay file
Can be used to (re)configure the FPGA while the OS is running (useful during development)
  Additional hardware added to system via daughter cards or mezzanine cards plugged into base board
  New FPGA configuration file is loaded which causes the FPGA hardware peripherals to change
  Partial reconfiguration changes the FPGA hardware peripherals
Overlays are the preferred methodology moving forward
Notes: Arria 10 can only do partial reconfig via overlay – no full reconfig (you will lose DDR controller), or reboot the board

## Slide 23: Device Tree Overlay Properties
Required properties
  target-path = full path where overlay will be inserted in live tree or target = phandle of insertion point
  address-cells and address-size = inherited from properties of parent node of insertion point
  firmware-name : name of an FPGA configuration file in the firmware search path (described in firmware class documentation)
  partial-fpga-config : boolean, used with FPGA partial reconfiguration, used with firmware-name to specify configuration file
  external-fpga-config : boolean, used if FPGA is already configured (or will be configured externally)
Optional properties
  region-unfreeze-timeout-us = max time (in microseconds) to wait for bridges to be enabled after the region has been programmed
  region-freeze-timeout-us = maximum time (in microseconds) to wait for bridges to be disabled before the region has been programmed
  config-complete-timeout-us = maximum time (in microseconds) to wait for the FPGA to go to user mode after the region has been programmed
Notes: Example will demonstrate this next slide

## Slide 24: Device Tree Overlay Use Cases
Full FPGA configuration (Example 1)
  Adds 2 FPGA peripherals
  Bridges controlled by FPGA Manager that configures FPGA
  FPGA Bridge devices not required for full reconfiguration
Full FPGA configuration to setup Partial Reconfiguration Regions, with hardware bridges (Example 2)
Partial reconfiguration with soft FPGA bridges (Example 3)
Notes: From fpga-regions.txt

## Slide 25: Device tree overlay – Example 1 – Full FPGA Configuration and Append to Base Tree
HPS
FPGA
fpga_region
Device Tree Overlay
jtag_uart
led_pio
HPS2FPGA / FPGA2HSP BRIDGES
soc_system.rbf
Notes: soc_system.rbf performs a full configuration of the FPGA and applies overlay to add jtag_uart and led_pio

## Slide 26: Device tree overlay – Example 1 – Full FPGA Configuration and Append to Base Tree
/dts-v1/ /plugin/;
/ {
fragment@0 {
target-path = "/soc/base_fpga_region";
#address-cells = <1>;
#size-cells = <1>;
__overlay__ {
#address-cells = <1>;
#size-cells = <1>;
firmware-name = "soc_system.rbf";
jtag_uart: serial@20000 {
compatible = "altr,juart-1.0";
reg = <0x20000 0x8>;
interrupt-parent = <&intc>;
interrupts = <0 42 4>;
};
led_pio: gpio@10040 {
compatible = "altr,pio-1.0";
reg = <0x10040 0x20>;
altr,gpio-bank-width = <4>;
#gpio-cells = <2>;
gpio-controller;
};
};
};
fragment@1 { // second child node
...
};
};
Contents of the overlay will be applied to target base_fpga_region under soc node in the live tree.
Use of the firmware-name property indicates that the FPGA should be (re)configured with the given .rbf file. Any bridges listed in base_fpga_region will first be disabled, then the FPGA is configured using the FPGA manager core.
If FPGA configuration is successful, the bridges are re-enabled and these child devices are populated to the live tree. If configuration fails, the bridges remain disabled and the overlay is rejected.
of_platform_populate is called and device drivers are probed.
1.
2.
3.
Notes: From Documentation/devicetree/bindings/overlay-notes.txt:
For target, use:
target=<phandle>; /* phandle target of the overlay */
or
target-path="/path"; /* target path of the overlay */
Using the non-phandle based target method allows one to use a base DT which does
not contain a __symbols__ node, i.e. it was not compiled with the -@ option.
The __symbols__ node is only required for the target=<phandle> method, since it
contains the information required to map from a phandle to a tree location.

## Slide 27: Device tree overlay – Example 2 – adding Partial Reconfiguration Regions
HPS
FPGA
fpga_region1 (Partial Reconfiguration Region 1)
HPS2FPGA / FPGA2HSP BRIDGES
fpga_region2 (Partial Reconfiguration Region 2)
fpga_bridge1_0
(freeze-bridge-controller)
fpga_bridge2_0
(freeze-bridge-controller)
base.rbf
Device Tree Overlay
Notes: base.rbf performs a full configuration of the FPGA and sets up 2 Partial Reconfig regions
FPGA BRIDGES are soft logic bridges used to gate traffic (i.e. disabled) while region is partially reconfigured

## Slide 28: Device tree overlay – Example 2 – adding Partial Reconfiguration Regions
/dts-v1/ /plugin/;
/ {
fragment@0 {
target-path = "/soc/base_fpga_region";
#address-cells = <1>;
#size-cells = <1>;
__overlay__ {
#address-cells = <1>;
#size-cells = <1>;
firmware-name = "base.rbf";
fpga_bridge1_0: fpga_bridge@4400 {
compatible = "altr,freeze-bridge-controller";
reg = <0x4400 0x10>;
};
fpga_bridge2_0: fpga_bridge@4420 {
compatible = "altr,freeze-bridge-controller";
reg = <0x4420 0x10>;
};
fpga_region1 {
compatible = "fpga-region";
fpga-bridges = <&fpga_bridge1_0>;
#address-cells = <0x1>;
#size-cells = <0x1>;
ranges;
};
fpga_region2 {
compatible = "fpga-region";
fpga-bridges = <&fpga_bridge2_0>;
#address-cells = <0x1>;
#size-cells = <0x1>;
ranges;
};
Contents of the overlay will be applied to target base_fpga_region under soc node in the live tree.
base.rbf configures the FPGA and sets up 2 Partial Reconfig Regions.
Each Region contains a soft FPGA bridge controlled by the freeze-bridge-controller driver.
Partial Reconfiguration Regions defined similar to base_fpga_region, using soft FPGA bridges.
1.
2.
3.
4.
Empty ranges property specifies that the parent and child address space is identical, and no address translation is required.

## Slide 29: Device tree overlay – Example 3 – Reprogram a Partial Reconfiguration Region
HPS
FPGA
fpga_region1 (Partial Reconfiguration Region 1)
HPS2FPGA / FPGA2HSP BRIDGES
fpga_region2 (Partial Reconfiguration Region 2)
fpga_bridge1_0
(freeze-bridge-controller)
fpga_bridge2_0
(freeze-bridge-controller)
soc_image1.rbf
Device Tree Overlay
Notes: soc_image1.rbf performs a partial configuration of the fpga_region1
FPGA BRIDGES are soft logic bridges used to gate traffic (i.e. disabled) while region is partially reconfigured

## Slide 30: Device tree overlay – Example 3 – Reprogram a Partial Reconfiguration Region
/dts-v1/ /plugin/;
/ {
fragment@0 {
target-path = "/soc/base_fpga_region/fpga_region1";
#address-cells = <1>;
#size-cells = <1>;
__overlay__ {
#address-cells = <1>;
#size-cells = <1>;
firmware-name = "soc_image1.rbf";
partial-fpga-config;
region-unfreeze-timeout-us = <4>;
region-freeze-timeout-us = <4>;
gpio@10040 {
compatible = "altr,pio-1.0";
reg = <0x10040 0x20>;
clocks = <0x2>;
altr,gpio-bank-width = <0x4>;
resetvalue = <0x0>;
#gpio-cells = <0x2>;
gpio-controller;
};
};
};
};
Contents of the overlay will be applied to target fpga_region1 under soc/base_fpga_region node in the live tree.
Use of the firmware-name property and boolean partial-fpga-config indicates that the FPGA will be partially reconfigured with the given .rbf file, targeting fpga_region1.
If FPGA configuration is successful, the bridges are re-enabled and the child devices are populated to the live tree. If configuration fails, the bridges remain disabled and the overlay is rejected.
1.
2.
3.

## Slide 31: Loading the Overlay in Linux
Makes use of Linux configfs to allow a userspace event to create a kernel object
  A configfs config_item is created with mkdir and destroyed with rmdir.
  See kernel source Documentation/filesystems/configfs/configfs.txt for complete details
This can be accomplished with an init script added to root filesystem (examples next 2 slides) or by manually executing the commands in the script
  SysVinit - /etc/init.d
  systemd - /lib/systemd/system
Copy .rbf and .dtb to /lib/firmware first
Can be used to (re)configure the FPGA only without appending the base device tree
  Replaces “cat” or “echo”-ing the .rbf to /dev/fpga0
Notes: Configfs must be enabled in the kernel build (make menuconfig or via a defconfig file)
This is enabled in socfpga_defconfig in 4.1.22-ltsi kernel source

## Slide 32: Example SysVInit script
#!/bin/sh # start() { echo "********************************************************************" echo "Applying overlay" echo "********************************************************************" mkdir /config mount -t configfs configfs /config mkdir /config/device-tree/overlays/my-board echo my-overlay.dtb > /config/device-tree/overlays/my-board/path } stop() { echo "********************************************************************" echo "Removing overlay" echo "********************************************************************" rmdir /config/device-tree/overlays/my-board } restart() { stop start } case "$1" in start) start ;; stop) stop ;; restart|reload) restart ;; *) echo "Usage: $0 {start|stop|restart}" exit 1 esac exit $?
On a SysVInit system, this script is saved in the /etc/init.d folder.
At system start up, /config directory is created and mounted to configfs; directory is created for overlay file and file name is appended to path file
At system shutdown, overlay directory is removed
1.
2.
S50devicetree_overlay
Notes: Path is a file that gets created by configfs when you create the my-board directory
We are copying the my_overlay.dtb file name to the path file
Default place to look is in /lib/firmware

## Slide 33: Example systemd script
[Unit]
Description=Devicetree Overlay Service
[Service]
ExecStart=/usr/bin/devicetree-overlay.sh
[Install]
WantedBy=multi-user.target
At system start up, /config directory is created and mounted to configfs; directory is created for overlay file and file name is appended to path file. At system shutdown, overlay directory is removed when unmounting /config
#!/bin/sh
mkdir /config
mount -t configfs configfs /config
mkdir /config/device-tree/overlays/my-board
echo my-overlay.dtb > /config/device-tree/overlays/my-board/path
/lib/systemd/system/devicetree-overlay.service
/usr/bin/devicetree-overlay.sh
Enable the service with
# systemctl enable devicetree-overlay.service
to create a symlink to /etc/systemd/system
1.
Notes: Path is a file that gets created by configfs when you create the my-board directory
We are copying the my_overlay.dtb file name to the path file
Default place to look is in /lib/firmware

## Slide 34: Applying Overlay Summary
Create overlay .dts file (use example as starting point). Base .dts file must use FPGA Regions framework.
Compile the overlay .dts to create the overlay .dtb
Copy .rbf (if used) and .dtb to /lib/firmware on target root filesystem
Create init script and copy to target root filesystem OR manually execute the commands in the script
Verify that the overlay was applied
  cat /config/device-tree/overlays/my-board/status
Notes: Configfs must be enabled in the kernel build (make menuconfig or via a defconfig file)
This is enabled in socfpga_defconfig in 4.1.22-ltsi kernel source

## Slide 35: Viewing Device Tree Info in Linux
Buses, devices, device classes, drivers are internal to the kernel but are exported to user space through the sysfs virtual filesystem.
Can be found in /sys (sysfs mounted in /sys)
  /sys/bus – lists buses
  /sys/devices – lists devices
  /sys/class – enumerates devices by class
View current system memory maps and all devices defined in device tree
  cat /proc/iomem
Additional information available in /proc/device-tree
  ls /proc/device-tree
Notes: Applicable for any device tree method (not just overlays)
A user space application can use these paths to verify that expected hardware exists

## Slide 36: Creating a Device Tree for a Custom Board

## Slide 37: Example device tree flow
Clone the Altera kernel repository
Create your board level .dts file (start with example from /arch/arm/boot/dts), and #include appropriate dtsi files in the kernel tree for your device (A10, C5, A5)
Copy to /arch/arm/boot/dts
  Typical naming convention is <soc-name>-<board-name>.dts
  Altera uses socfpga_<device-family>_<board-name>.dts
    socfpga_cyclone5_sockit.dts
    socfpga_arria10_socdk_nand.dts
Modify the kernel makefile to build your .dtb during kernel build
  arch/arm/boot/dts/Makefile
  add dtb-$(CONFIG_ARCH_SOCFPGA) += socfpga_cyclone5_myboard.dtb
OR, build separately after kernel build
  export ARCH and CROSS_COMPILE variables first or as part of make if not already done
  make ARCH=arm CONFIG_DTB_SOURCE=arch/arm/boot/dts/my-board.dts my-board.dtb

## Slide 38: Common Device Tree Problems
This is by no means an exhaustive list
Kernel hangs
  often (but not always) indicates a problem with the device tree
Driver fails to load
  Check for device tree entry with compatible string for driver
  Check that required properties are fully listed in the device tree as defined in the Device Tree binding .txt file in kernel source directory (Documentation/devicetree/bindings)
Device driver loads but device not visible in Linux
  Is the device enabled in the board level device tree? Many devices are disabled by default in the common .dtsi files.

## Slide 39: References
www.free-electrons.com
  Linux kernel and driver development course
  Device Tree for Dummies
Linux kernel source Documentation folder
Cyclone V Handbook
http://elinux.org/Device_Tree_Usage
ePAPR v1.1

## Slide 40: Appendix – Fully Annotated Example Device Tree

## Slide 41: Annotated Device Tree Example
To create a complete device tree from scratch, one would need to know about all of the hardware available in the system
Fortunately, the hierarchical device trees provided in the kernel source tree have already defined this for us for the Altera SoC FPGAs
The following example uses the Arrow SoCKit device tree example provided in the kernel source tree at arch/arm/boot/dts/socfpga_cyclone5_sockit.dts
The following slides will attempt to clearly define all the components of this device tree and describe what is required vs. optional
Consider changing to Chameleon96 board example since the SoCKit device tree example does not use FPGA Regions.

## Slide 42: Annotated Device Tree Example
The Cyclone V Hard Processor System Technical Reference Manual lists the HPS peripherals:
MPU subsystem featuring a single- or dual-core ARM Cortex-A9 MPCore processor
General-purpose direct memory access (DMA) controller
Two ethernet media access controllers (EMACs)
Two USB 2.0 on-the-go (OTG) controllers
NAND flash controller
Quad SPI flash controller
Secure digital/multimedia card (SD/MMC) controller
Two serial peripheral interface (SPI) master controllers
Two SPI slave controllers
Four inter-integrated circuit (I2C) controllers
64 KB on-chip RAM
64 KB on-chip boot ROM
Two UARTs
Four timers
Two watchdog timers
Three general-purpose I/O (GPIO) interfaces
Two controller area network (CAN) controllers
ARM Coresight™ debug components:
Debug access port (DAP)
Trace port interface unit (TPIU)
System trace macrocell (STM)
Program trace macrocell (PTM)
Embedded trace router (ETR)
Embedded cross trigger (ECT)
System manager
Clock manager
Reset manager
Scan manager
FPGA manager
SDRAM controller subsystem

## Slide 43: Annotated Device Tree Example
The base addresses for these peripherals are further defined in the Cyclone V SoC HPS Address Map and Register Definitions
All of these peripherals should be defined in the device tree. In this example they are defined in socfpga.dtsi.
Recall from the previous slide example how the hierarchy works using the kernel source tree dtsi files:
socfpga_cyclone5_sockit.dts
socfpga_cyclone5.dtsi
socfpga.dtsi
skeleton.dtsi

## Slide 44: socfpga_cyclone5_sockit.dts (1/3)
/*
* Copyright (C) 2013 Steffen Trumtrar <s.trumtrar@pengutronix.de>
*
* This program is free software; you can redistribute it and/or modify
* it under the terms of the GNU General Public License as published by
* the Free Software Foundation; either version 2 of the License, or
* (at your option) any later version.
*
* This program is distributed in the hope that it will be useful,
* but WITHOUT ANY WARRANTY; without even the implied warranty of
* MERCHANTABILITY or FITNESS FOR A PARTICULAR PURPOSE. See the
* GNU General Public License for more details.
*
* You should have received a copy of the GNU General Public License
* along with this program. If not, see <http://www.gnu.org/licenses/>.
*/
#include "socfpga_cyclone5.dtsi"
/ {
model = "Terasic SoCkit";
compatible = "altr,socfpga-cyclone5", "altr,socfpga";
chosen {
bootargs = "earlyprintk";
stdout-path = "serial0:115200n8";
};
memory {
name = "memory";
device_type = "memory";
reg = <0x0 0x40000000>; /* 1GB */
};
CONTINUED...
Include this Cyclone V device tree when compiling
Name of the system; can be used by OS to determine how to run on this machine or perform various checks
model: string to specify mfr. model number of device
memory: required for all device trees, specifies size and location of RAM
chosen: Default kernel command line arguments

## Slide 45: socfpga_cyclone5_sockit.dts (2/3)
aliases {
/* this allow the ethaddr uboot environmnet variable contents
* to be added to the gmac1 device tree blob.
*/
ethernet0 = &gmac1;
};
regulator_3_3v: vcc3p3-regulator {
compatible = "regulator-fixed";
regulator-name = "VCC3P3";
regulator-min-microvolt = <3300000>;
regulator-max-microvolt = <3300000>;
};
};
&gmac1 {
status = "okay";
phy-mode = "rgmii";
rxd0-skew-ps = <0>;
rxd1-skew-ps = <0>;
rxd2-skew-ps = <0>;
rxd3-skew-ps = <0>;
txen-skew-ps = <0>;
txc-skew-ps = <2600>;
rxdv-skew-ps = <0>;
rxc-skew-ps = <2000>;
};
&mmc0 {
vmmc-supply = <&regulator_3_3v>;
vqmmc-supply = <&regulator_3_3v>;
};
CONTINUED...
aliases: allows a node to be referred to by the alias name.
Note that there is also an aliases node in socfpga.dtsi that sets ethernet1 = &gmac1, but this setting at the highest level in the hierarchy overrides the setting in the lower level. Only gmac1 is used on the SoCKit board.
aliases node must be at the root of the device tree
regulator entry allows for control of voltage regulators. See Documentation/devicetree/bindings/regulator/regulator.txt for additional options not used here.
gmac1 is enabled with status = “okay”. Use of phandle &gmac1 allows this to be referenced from socfpga.dtsi.
phandle to the regulator to use for vmmc for the mmc controller. If specified, probe is deferred until this regulator is found.

## Slide 46: socfpga_cyclone5_sockit.dts (3/3)
&usb1 {
status = "okay";
};
&qspi {
flash0: n25q00@0 {
#address-cells = <1>;
#size-cells = <1>;
compatible = "n25q00";
reg = <0>; /* chip select */
spi-max-frequency = <100000000>;
m25p,fast-read;
page-size = <256>;
block-size = <16>; /* 2^16, 64KB */
read-delay = <4>; /* delay value in read data capture register */
tshsl-ns = <50>;
tsd2d-ns = <50>;
tchsh-ns = <4>;
tslch-ns = <4>;
partition@qspi-boot {
/* 8MB for raw data. */
label = "Flash 0 Raw Data";
reg = <0x0 0x800000>;
};
partition@qspi-rootfs {
/* 120MB for jffs2 data. */
label = "Flash 0 jffs2 Filesystem";
reg = <0x800000 0x7800000>;
};
};
};
usb1 is enabled with status = “okay

## Slide 47: socfpga_cyclone5.dtsi (1/2)
/*
* Copyright Altera Corporation (C) 2012,2014. All rights reserved.
*
* This program is free software; you can redistribute it and/or modify
* it under the terms and conditions of the GNU General Public License,
* version 2, as published by the Free Software Foundation.
*
* This program is distributed in the hope it will be useful, but WITHOUT
* ANY WARRANTY; without even the implied warranty of MERCHANTABILITY or
* FITNESS FOR A PARTICULAR PURPOSE. See the GNU General Public License for
* more details.
*
* You should have received a copy of the GNU General Public License along with
* this program. If not, see <http://www.gnu.org/licenses/>.
*/
/dts-v1/;
/* First 4KB has trampoline code for secondary cores. */
/memreserve/ 0x00000000 0x0001000;
#include "socfpga.dtsi"
/ {
soc {
clkmgr@ffd04000 {
clocks {
osc1 {
clock-frequency = <25000000>;
};
};
};
CONTINUED...
memreserve marks this memory space as reserved from the kernel
Include this common socfpga device tree when compiling

## Slide 48: socfpga_cyclone5.dtsi (2/2)
mmc0: dwmmc0@ff704000 {
num-slots = <1>;
broken-cd;
bus-width = <4>;
cap-mmc-highspeed;
cap-sd-highspeed;
};
ethernet@ff702000 {
phy-mode = "rgmii";
phy-addr = <0xffffffff>; /* probe for phy addr */
status = "okay";
};
sysmgr@ffd08000 {
cpu1-start-addr = <0xffd080c4>;
};
};
};
&watchdog0 {
status = "okay";
};
watchdog0 is enabled with status = “okay

## Slide 49: socfpga.dtsi (1/28)
/*
* Copyright Altera Corporation (C) 2012-2014. All rights reserved.
*
* This program is free software; you can redistribute it and/or modify
* it under the terms and conditions of the GNU General Public License,
* version 2, as published by the Free Software Foundation.
*
* This program is distributed in the hope it will be useful, but WITHOUT
* ANY WARRANTY; without even the implied warranty of MERCHANTABILITY or
* FITNESS FOR A PARTICULAR PURPOSE. See the GNU General Public License for
* more details.
*
* You should have received a copy of the GNU General Public License along with
* this program. If not, see <http://www.gnu.org/licenses/>.
*/
#include "skeleton.dtsi"
#include <dt-bindings/reset/altr,rst-mgr.h>
/ {
#address-cells = <1>;
#size-cells = <1>;
aliases {
ethernet0 = &gmac0;
ethernet1 = &gmac1;
serial0 = &uart0;
serial1 = &uart1;
timer0 = &timer0;
timer1 = &timer1;
timer2 = &timer2;
timer3 = &timer3;
};
CONTINUED...

## Slide 50: socfpga.dtsi (2/28)
cpus {
#address-cells = <1>;
#size-cells = <0>;
enable-method = "altr,socfpga-smp";
cpu@0 {
compatible = "arm,cortex-a9";
device_type = "cpu";
reg = <0>;
next-level-cache = <&L2>;
};
cpu@1 {
compatible = "arm,cortex-a9";
device_type = "cpu";
reg = <1>;
next-level-cache = <&L2>;
};
};
intc: intc@fffed000 {
compatible = "arm,cortex-a9-gic";
#interrupt-cells = <3>;
interrupt-controller;
reg = <0xfffed000 0x1000>,
<0xfffec100 0x100>;
};
CONTINUED...

## Slide 51: socfpga.dtsi (3/28)
soc {
#address-cells = <1>;
#size-cells = <1>;
compatible = "simple-bus";
device_type = "soc";
interrupt-parent = <&intc>;
ranges;
amba {
compatible = "arm,amba-bus";
#address-cells = <1>;
#size-cells = <1>;
ranges;
pdma: pdma@ffe01000 {
compatible = "arm,pl330", "arm,primecell";
reg = <0xffe01000 0x1000>;
interrupts = <0 104 4>,
<0 105 4>,
<0 106 4>,
<0 107 4>,
<0 108 4>,
<0 109 4>,
<0 110 4>,
<0 111 4>;
#dma-cells = <1>;
#dma-channels = <8>;
#dma-requests = <32>;
clocks = <&l4_main_clk>;
clock-names = "apb_pclk";
};
};
CONTINUED...

## Slide 52: socfpga.dtsi (4/28)
base_fpga_region: base-fpga-region {
compatible = "fpga-region";
fpga-mgr = <&fpga_mgr>;
#address-cells = <0x1>;
#size-cells = <0x1>;
};
can0: can@ffc00000 {
compatible = "bosch,d_can";
reg = <0xffc00000 0x1000>;
interrupts = <0 131 4>, <0 132 4>, <0 133 4>, <0 134 4>;
clocks = <&can0_clk>;
status = "disabled";
};
can1: can@ffc01000 {
compatible = "bosch,d_can";
reg = <0xffc01000 0x1000>;
interrupts = <0 135 4>, <0 136 4>, <0 137 4>, <0 138 4>;
clocks = <&can1_clk>;
status = "disabled";
};
clkmgr@ffd04000 {
compatible = "altr,clk-mgr";
reg = <0xffd04000 0x1000>;
clocks {
#address-cells = <1>;
#size-cells = <0>;
CONTINUED...

## Slide 53: socfpga.dtsi (5/28)
osc1: osc1 {
#clock-cells = <0>;
compatible = "fixed-clock";
};
osc2: osc2 {
#clock-cells = <0>;
compatible = "fixed-clock";
};
f2s_periph_ref_clk: f2s_periph_ref_clk {
#clock-cells = <0>;
compatible = "fixed-clock";
};
f2s_sdram_ref_clk: f2s_sdram_ref_clk {
#clock-cells = <0>;
compatible = "fixed-clock";
};
main_pll: main_pll {
#address-cells = <1>;
#size-cells = <0>;
#clock-cells = <0>;
compatible = "altr,socfpga-pll-clock";
clocks = <&osc1>;
reg = <0x40>;
mpuclk: mpuclk {
#clock-cells = <0>;
compatible = "altr,socfpga-perip-clk";
clocks = <&main_pll>;
div-reg = <0xe0 0 9>;
reg = <0x48>;
}; CONTINUED...

## Slide 54: socfpga.dtsi (6/28)
mainclk: mainclk {
#clock-cells = <0>;
compatible = "altr,socfpga-perip-clk";
clocks = <&main_pll>;
div-reg = <0xe4 0 9>;
reg = <0x4C>;
};
dbg_base_clk: dbg_base_clk {
#clock-cells = <0>;
compatible = "altr,socfpga-perip-clk";
clocks = <&main_pll>, <&osc1>;
div-reg = <0xe8 0 9>;
reg = <0x50>;
};
main_qspi_clk: main_qspi_clk {
#clock-cells = <0>;
compatible = "altr,socfpga-perip-clk";
clocks = <&main_pll>;
reg = <0x54>;
};
main_nand_sdmmc_clk: main_nand_sdmmc_clk {
#clock-cells = <0>;
compatible = "altr,socfpga-perip-clk";
clocks = <&main_pll>;
reg = <0x58>;
};
cfg_h2f_usr0_clk: cfg_h2f_usr0_clk {
#clock-cells = <0>;
compatible = "altr,socfpga-perip-clk";
clocks = <&main_pll>;
reg = <0x5C>;
};
}; CONTINUED...

## Slide 55: socfpga.dtsi (7/28)
periph_pll: periph_pll {
#address-cells = <1>;
#size-cells = <0>;
#clock-cells = <0>;
compatible = "altr,socfpga-pll-clock";
clocks = <&osc1>, <&osc2>, <&f2s_periph_ref_clk>;
reg = <0x80>;
emac0_clk: emac0_clk {
#clock-cells = <0>;
compatible = "altr,socfpga-perip-clk";
clocks = <&periph_pll>;
reg = <0x88>;
};
emac1_clk: emac1_clk {
#clock-cells = <0>;
compatible = "altr,socfpga-perip-clk";
clocks = <&periph_pll>;
reg = <0x8C>;
};
per_qspi_clk: per_qsi_clk {
#clock-cells = <0>;
compatible = "altr,socfpga-perip-clk";
clocks = <&periph_pll>;
reg = <0x90>;
};
per_nand_mmc_clk: per_nand_mmc_clk {
#clock-cells = <0>;
compatible = "altr,socfpga-perip-clk";
clocks = <&periph_pll>;
reg = <0x94>;
}; CONTINUED...

## Slide 56: socfpga.dtsi (8/28)
per_base_clk: per_base_clk {
#clock-cells = <0>;
compatible = "altr,socfpga-perip-clk";
clocks = <&periph_pll>;
reg = <0x98>;
};
h2f_usr1_clk: h2f_usr1_clk {
#clock-cells = <0>;
compatible = "altr,socfpga-perip-clk";
clocks = <&periph_pll>;
reg = <0x9C>;
};
};
sdram_pll: sdram_pll {
#address-cells = <1>;
#size-cells = <0>;
#clock-cells = <0>;
compatible = "altr,socfpga-pll-clock";
clocks = <&osc1>, <&osc2>, <&f2s_sdram_ref_clk>;
reg = <0xC0>;
ddr_dqs_clk: ddr_dqs_clk {
#clock-cells = <0>;
compatible = "altr,socfpga-perip-clk";
clocks = <&sdram_pll>;
reg = <0xC8>;
};
ddr_2x_dqs_clk: ddr_2x_dqs_clk {
#clock-cells = <0>;
compatible = "altr,socfpga-perip-clk";
clocks = <&sdram_pll>;
reg = <0xCC>;
}; CONTINUED...

## Slide 57: socfpga.dtsi (9/28)
ddr_dq_clk: ddr_dq_clk {
#clock-cells = <0>;
compatible = "altr,socfpga-perip-clk";
clocks = <&sdram_pll>;
reg = <0xD0>;
};
h2f_usr2_clk: h2f_usr2_clk {
#clock-cells = <0>;
compatible = "altr,socfpga-perip-clk";
clocks = <&sdram_pll>;
reg = <0xD4>;
};
};
mpu_periph_clk: mpu_periph_clk {
#clock-cells = <0>;
compatible = "altr,socfpga-perip-clk";
clocks = <&mpuclk>;
fixed-divider = <4>;
};
mpu_l2_ram_clk: mpu_l2_ram_clk {
#clock-cells = <0>;
compatible = "altr,socfpga-perip-clk";
clocks = <&mpuclk>;
fixed-divider = <2>;
};
l4_main_clk: l4_main_clk {
#clock-cells = <0>;
compatible = "altr,socfpga-gate-clk";
clocks = <&mainclk>;
clk-gate = <0x60 0>;
}; CONTINUED...

## Slide 58: socfpga.dtsi (10/28)
l3_main_clk: l3_main_clk {
#clock-cells = <0>;
compatible = "altr,socfpga-perip-clk";
clocks = <&mainclk>;
fixed-divider = <1>;
};
l3_mp_clk: l3_mp_clk {
#clock-cells = <0>;
compatible = "altr,socfpga-gate-clk";
clocks = <&mainclk>;
div-reg = <0x64 0 2>;
clk-gate = <0x60 1>;
};
l3_sp_clk: l3_sp_clk {
#clock-cells = <0>;
compatible = "altr,socfpga-gate-clk";
clocks = <&l3_mp_clk>;
div-reg = <0x64 2 2>;
};
l4_mp_clk: l4_mp_clk {
#clock-cells = <0>;
compatible = "altr,socfpga-gate-clk";
clocks = <&mainclk>, <&per_base_clk>;
div-reg = <0x64 4 3>;
clk-gate = <0x60 2>;
};
l4_sp_clk: l4_sp_clk {
#clock-cells = <0>;
compatible = "altr,socfpga-gate-clk";
clocks = <&mainclk>, <&per_base_clk>;
div-reg = <0x64 7 3>;
clk-gate = <0x60 3>;
}; CONTINUED...

## Slide 59: socfpga.dtsi (11/28)
dbg_at_clk: dbg_at_clk {
#clock-cells = <0>;
compatible = "altr,socfpga-gate-clk";
clocks = <&dbg_base_clk>;
div-reg = <0x68 0 2>;
clk-gate = <0x60 4>;
};
dbg_clk: dbg_clk {
#clock-cells = <0>;
compatible = "altr,socfpga-gate-clk";
clocks = <&dbg_at_clk>;
div-reg = <0x68 2 2>;
clk-gate = <0x60 5>;
};
dbg_trace_clk: dbg_trace_clk {
#clock-cells = <0>;
compatible = "altr,socfpga-gate-clk";
clocks = <&dbg_base_clk>;
div-reg = <0x6C 0 3>;
clk-gate = <0x60 6>;
};
dbg_timer_clk: dbg_timer_clk {
#clock-cells = <0>;
compatible = "altr,socfpga-gate-clk";
clocks = <&dbg_base_clk>;
clk-gate = <0x60 7>;
};
CONTINUED...

## Slide 60: socfpga.dtsi (12/28)
cfg_clk: cfg_clk {
#clock-cells = <0>;
compatible = "altr,socfpga-gate-clk";
clocks = <&cfg_h2f_usr0_clk>;
clk-gate = <0x60 8>;
};
h2f_user0_clk: h2f_user0_clk {
#clock-cells = <0>;
compatible = "altr,socfpga-gate-clk";
clocks = <&cfg_h2f_usr0_clk>;
clk-gate = <0x60 9>;
};
emac_0_clk: emac_0_clk {
#clock-cells = <0>;
compatible = "altr,socfpga-gate-clk";
clocks = <&emac0_clk>;
clk-gate = <0xa0 0>;
};
emac_1_clk: emac_1_clk {
#clock-cells = <0>;
compatible = "altr,socfpga-gate-clk";
clocks = <&emac1_clk>;
clk-gate = <0xa0 1>;
};
usb_mp_clk: usb_mp_clk {
#clock-cells = <0>;
compatible = "altr,socfpga-gate-clk";
clocks = <&per_base_clk>;
clk-gate = <0xa0 2>;
div-reg = <0xa4 0 3>;
}; CONTINUED...

## Slide 61: socfpga.dtsi (13/28)
spi_m_clk: spi_m_clk {
#clock-cells = <0>;
compatible = "altr,socfpga-gate-clk";
clocks = <&per_base_clk>;
clk-gate = <0xa0 3>;
div-reg = <0xa4 3 3>;
};
can0_clk: can0_clk {
#clock-cells = <0>;
compatible = "altr,socfpga-gate-clk";
clocks = <&per_base_clk>;
clk-gate = <0xa0 4>;
div-reg = <0xa4 6 3>;
};
can1_clk: can1_clk {
#clock-cells = <0>;
compatible = "altr,socfpga-gate-clk";
clocks = <&per_base_clk>;
clk-gate = <0xa0 5>;
div-reg = <0xa4 9 3>;
};
gpio_db_clk: gpio_db_clk {
#clock-cells = <0>;
compatible = "altr,socfpga-gate-clk";
clocks = <&per_base_clk>;
clk-gate = <0xa0 6>;
div-reg = <0xa8 0 24>;
};
CONTINUED...

## Slide 62: socfpga.dtsi (14/28)
h2f_user1_clk: h2f_user1_clk {
#clock-cells = <0>;
compatible = "altr,socfpga-gate-clk";
clocks = <&h2f_usr1_clk>;
clk-gate = <0xa0 7>;
};
sdmmc_clk: sdmmc_clk {
#clock-cells = <0>;
compatible = "altr,socfpga-gate-clk";
clocks = <&f2s_periph_ref_clk>, <&main_nand_sdmmc_clk>, <&per_nand_mmc_clk>;
clk-gate = <0xa0 8>;
clk-phase = <0 135>;
};
sdmmc_clk_divided: sdmmc_clk_divided {
#clock-cells = <0>;
compatible = "altr,socfpga-gate-clk";
clocks = <&sdmmc_clk>;
clk-gate = <0xa0 8>;
fixed-divider = <4>;
};
nand_x_clk: nand_x_clk {
#clock-cells = <0>;
compatible = "altr,socfpga-gate-clk";
clocks = <&f2s_periph_ref_clk>, <&main_nand_sdmmc_clk>, <&per_nand_mmc_clk>;
clk-gate = <0xa0 9>;
};
nand_clk: nand_clk {
#clock-cells = <0>;
compatible = "altr,socfpga-gate-clk";
clocks = <&f2s_periph_ref_clk>, <&main_nand_sdmmc_clk>, <&per_nand_mmc_clk>;
clk-gate = <0xa0 10>;
fixed-divider = <4>;
}; CONTINUED...

## Slide 63: socfpga.dtsi (15/28)
qspi_clk: qspi_clk {
#clock-cells = <0>;
compatible = "altr,socfpga-gate-clk";
clocks = <&f2s_periph_ref_clk>, <&main_qspi_clk>, <&per_qspi_clk>;
clk-gate = <0xa0 11>;
};
};
};
fpga_bridge0: fpga-bridge@ff400000 {
compatible = "altr,socfpga-lwhps2fpga-bridge";
reg = <0xff400000 0x100000>;
resets = <&rst LWHPS2FPGA_RESET>;
reset-names = "lwhps2fpga";
clocks = <&l4_main_clk>;
};
fpga_bridge1: fpga-bridge@ff500000 {
compatible = "altr,socfpga-hps2fpga-bridge";
reg = <0xff500000 0x10000>;
resets = <&rst HPS2FPGA_RESET>;
reset-names = "hps2fpga";
clocks = <&l4_main_clk>;
};
fpga_bridge2: fpga-bridge@ff600000 {
compatible = "altr,socfpga-fpga2hps-bridge";
reg = <0xff600000 0x100000>;
resets = <&rst FPGA2HPS_RESET>;
reset-names = "fpga2hps";
clocks = <&l4_main_clk>;
};
fpga_bridge3: fpga2sdram-bridge {
compatible = "altr,socfpga-fpga2sdram-bridge";
}; CONTINUED...

## Slide 64: socfpga.dtsi (16/28)
fpga_mgr: fpga-mgr@ff706000 {
compatible = "altr,socfpga-fpga-mgr";
reg = <0xff706000 0x1000
0xffb90000 0x20>;
interrupts = <0 175 4>;
};
gmac0: ethernet@ff700000 {
compatible = "altr,socfpga-stmmac", "snps,dwmac-3.70a", "snps,dwmac";
altr,sysmgr-syscon = <&sysmgr 0x60 0>;
reg = <0xff700000 0x2000>;
interrupts = <0 115 4>;
interrupt-names = "macirq";
mac-address = [00 00 00 00 00 00];/* Filled in by U-Boot */
clocks = <&emac0_clk>;
clock-names = "stmmaceth";
resets = <&rst EMAC0_RESET>;
reset-names = "stmmaceth";
snps,multicast-filter-bins = <256>;
snps,perfect-filter-entries = <128>;
tx-fifo-depth = <4096>;
rx-fifo-depth = <4096>;
status = "disabled";
};
CONTINUED...

## Slide 65: socfpga.dtsi (17/28)
gmac1: ethernet@ff702000 {
compatible = "altr,socfpga-stmmac", "snps,dwmac-3.70a", "snps,dwmac";
altr,sysmgr-syscon = <&sysmgr 0x60 2>;
reg = <0xff702000 0x2000>;
interrupts = <0 120 4>;
interrupt-names = "macirq";
mac-address = [00 00 00 00 00 00];/* Filled in by U-Boot */
clocks = <&emac1_clk>;
clock-names = "stmmaceth";
resets = <&rst EMAC1_RESET>;
reset-names = "stmmaceth";
snps,multicast-filter-bins = <256>;
snps,perfect-filter-entries = <128>;
tx-fifo-depth = <4096>;
rx-fifo-depth = <4096>;
status = "disabled";
};
i2c0: i2c@ffc04000 {
#address-cells = <1>;
#size-cells = <0>;
compatible = "snps,designware-i2c";
reg = <0xffc04000 0x1000>;
clocks = <&l4_sp_clk>;
interrupts = <0 158 0x4>;
status = "disabled";
};
i2c1: i2c@ffc05000 {
#address-cells = <1>;
#size-cells = <0>;
compatible = "snps,designware-i2c";
reg = <0xffc05000 0x1000>;
clocks = <&l4_sp_clk>;
interrupts = <0 159 0x4>;
status = "disabled";
}; CONTINUED...

## Slide 66: socfpga.dtsi (18/28)
i2c2: i2c@ffc06000 {
#address-cells = <1>;
#size-cells = <0>;
compatible = "snps,designware-i2c";
reg = <0xffc06000 0x1000>;
clocks = <&l4_sp_clk>;
interrupts = <0 160 0x4>;
status = "disabled";
};
i2c3: i2c@ffc07000 {
#address-cells = <1>;
#size-cells = <0>;
compatible = "snps,designware-i2c";
reg = <0xffc07000 0x1000>;
clocks = <&l4_sp_clk>;
interrupts = <0 161 0x4>;
status = "disabled";
};
gpio0: gpio@ff708000 {
#address-cells = <1>;
#size-cells = <0>;
compatible = "snps,dw-apb-gpio";
reg = <0xff708000 0x1000>;
clocks = <&l4_mp_clk>;
status = "disabled";
CONTINUED...

## Slide 67: socfpga.dtsi (19/28)
porta: gpio-controller@0 {
compatible = "snps,dw-apb-gpio-port";
gpio-controller;
#gpio-cells = <2>;
snps,nr-gpios = <29>;
reg = <0>;
interrupt-controller;
#interrupt-cells = <2>;
interrupts = <0 164 4>;
};
};
gpio1: gpio@ff709000 {
#address-cells = <1>;
#size-cells = <0>;
compatible = "snps,dw-apb-gpio";
reg = <0xff709000 0x1000>;
clocks = <&l4_mp_clk>;
status = "disabled";
portb: gpio-controller@0 {
compatible = "snps,dw-apb-gpio-port";
gpio-controller;
#gpio-cells = <2>;
snps,nr-gpios = <29>;
reg = <0>;
interrupt-controller;
#interrupt-cells = <2>;
interrupts = <0 165 4>;
};
};
CONTINUED...

## Slide 68: socfpga.dtsi (20/28)
gpio2: gpio@ff70a000 {
#address-cells = <1>;
#size-cells = <0>;
compatible = "snps,dw-apb-gpio";
reg = <0xff70a000 0x1000>;
clocks = <&l4_mp_clk>;
status = "disabled";
portc: gpio-controller@0 {
compatible = "snps,dw-apb-gpio-port";
gpio-controller;
#gpio-cells = <2>;
snps,nr-gpios = <27>;
reg = <0>;
interrupt-controller;
#interrupt-cells = <2>;
interrupts = <0 166 4>;
};
};
sdr: sdr@ffc25000 {
compatible = "altr,sdr-ctl", "syscon";
reg = <0xffc25000 0x1000>;
};
sdramedac {
compatible = "altr,sdram-edac";
altr,sdr-syscon = <&sdr>;
interrupts = <0 39 4>;
};
CONTINUED...

## Slide 69: socfpga.dtsi (21/28)
L2: l2-cache@fffef000 {
compatible = "arm,pl310-cache", "syscon";
reg = <0xfffef000 0x1000>;
interrupts = <0 38 0x04>;
cache-unified;
cache-level = <2>;
arm,tag-latency = <1 1 1>;
arm,data-latency = <2 1 1>;
prefetch-data = <1>;
prefetch-instr = <1>;
};
l3regs@0xff800000 {
compatible = "altr,l3regs", "syscon";
reg = <0xff800000 0x1000>;
};
mmc: dwmmc0@ff704000 {
compatible = "altr,socfpga-dw-mshc";
reg = <0xff704000 0x1000>;
interrupts = <0 139 4>;
fifo-depth = <0x400>;
#address-cells = <1>;
#size-cells = <0>;
clocks = <&l4_mp_clk>, <&sdmmc_clk_divided>;
clock-names = "biu", "ciu";
};
ocram: sram@ffff0000 {
compatible = "mmio-sram";
reg = <0xffff0000 0x10000>;
};
CONTINUED...

## Slide 70: socfpga.dtsi (22/28)
nand: nand@ff900000 {
#address-cells = <1>;
#size-cells = <1>;
compatible = "denali,denali-nand-dt";
reg = <0xff900000 0x100000>, <0xffb80000 0x10000>;
reg-names = "nand_data", "denali_reg";
interrupts = <0 144 4>;
dma-mask = <0xffffffff>;
clocks = <&nand_clk>;
have-hw-ecc-fixup;
status = "disabled";
partition@nand-boot {
/* 8MB for raw data. */
label = "NAND Flash Boot Area 8MB";
reg = <0x0 0x800000>;
};
partition@nand-rootfs {
/* 128MB jffs2 root filesystem. */
label = "NAND Flash jffs2 Root Filesystem 128MB";
reg = <0x800000 0x8000000>;
};
partition@nand-128 {
label = "NAND Flash 128 MB";
reg = <0x8800000 0x8000000>;
};
partition@nand-64 {
label = "NAND Flash 64 MB";
reg = <0x10800000 0x4000000>;
};
partition@nand-32 {
label = "NAND Flash 32 MB";
reg = <0x14800000 0x2000000>;
}; CONTINUED...

## Slide 71: socfpga.dtsi (23/28)
partition@nand-16 {
label = "NAND Flash 16 MB";
reg = <0x16800000 0x1000000>;
};
};
l2edac@xffd08140 {
compatible = "altr,l2-edac";
reg = <0xffd08140 0x4>;
interrupts = <0 36 1>, <0 37 1>;
};
ocramedac@ffd08144 {
compatible = "altr,ocram-edac";
reg = <0xffd08144 0x4>;
iram = <&ocram>;
interrupts = <0 178 1>, <0 179 1>;
};
qspi: spi@ff705000 {
compatible = "cdns,qspi-nor";
#address-cells = <1>;
#size-cells = <0>;
reg = <0xff705000 0x1000>,
<0xffa00000 0x1000>;
interrupts = <0 151 4>;
clocks = <&qspi_clk>;
is-decoded-cs = <1>;
fifo-depth = <128>;
status = "disabled";
m25p,fast-read;
};
CONTINUED...

## Slide 72: socfpga.dtsi (24/28)
spi0: spi@fff00000 {
compatible = "snps,dw-apb-ssi";
#address-cells = <1>;
#size-cells = <0>;
reg = <0xfff00000 0x1000>;
interrupts = <0 154 4>;
num-cs = <4>;
tx-dma-channel = <&pdma 16>;
rx-dma-channel = <&pdma 17>;
clocks = <&per_base_clk>;
status = "disabled";
};
scu: snoop-control-unit@fffec000 {
compatible = "arm,cortex-a9-scu";
reg = <0xfffec000 0x100>;
};
spi1: spi@fff01000 {
compatible = "snps,dw-apb-ssi";
#address-cells = <1>;
#size-cells = <0>;
reg = <0xfff01000 0x1000>;
interrupts = <0 155 4>;
num-cs = <4>;
tx-dma-channel = <&pdma 20>;
rx-dma-channel = <&pdma 21>;
clocks = <&per_base_clk>;
status = "disabled";
};
CONTINUED...

## Slide 73: socfpga.dtsi (25/28)
/* Local timer */
timer@fffec600 {
compatible = "arm,cortex-a9-twd-timer";
reg = <0xfffec600 0x100>;
interrupts = <1 13 0xf04>;
clocks = <&mpu_periph_clk>;
};
timer0: timer0@ffc08000 {
compatible = "snps,dw-apb-timer";
interrupts = <0 167 4>;
reg = <0xffc08000 0x1000>;
clocks = <&l4_sp_clk>;
clock-names = "timer";
};
timer1: timer1@ffc09000 {
compatible = "snps,dw-apb-timer";
interrupts = <0 168 4>;
reg = <0xffc09000 0x1000>;
clocks = <&l4_sp_clk>;
clock-names = "timer";
};
timer2: timer2@ffd00000 {
compatible = "snps,dw-apb-timer";
interrupts = <0 169 4>;
reg = <0xffd00000 0x1000>;
clocks = <&osc1>;
clock-names = "timer";
};
CONTINUED...

## Slide 74: socfpga.dtsi (26/28)
timer3: timer3@ffd01000 {
compatible = "snps,dw-apb-timer";
interrupts = <0 170 4>;
reg = <0xffd01000 0x1000>;
clocks = <&osc1>;
clock-names = "timer";
};
uart0: serial0@ffc02000 {
compatible = "snps,dw-apb-uart";
reg = <0xffc02000 0x1000>;
interrupts = <0 162 4>;
reg-shift = <2>;
reg-io-width = <4>;
clocks = <&l4_sp_clk>;
dmas = <&pdma 28>,
<&pdma 29>;
dma-names = "tx", "rx";
};
uart1: serial1@ffc03000 {
compatible = "snps,dw-apb-uart";
reg = <0xffc03000 0x1000>;
interrupts = <0 163 4>;
reg-shift = <2>;
reg-io-width = <4>;
clocks = <&l4_sp_clk>;
dmas = <&pdma 30>,
<&pdma 31>;
dma-names = "tx", "rx";
};
CONTINUED...

## Slide 75: socfpga.dtsi (27/28)
rst: rstmgr@ffd05000 {
#reset-cells = <1>;
compatible = "altr,rst-mgr";
reg = <0xffd05000 0x1000>;
altr,modrst-offset = <0x10>;
};
usbphy0: usbphy@0 {
#phy-cells = <0>;
compatible = "usb-nop-xceiv";
status = "okay";
};
usb0: usb@ffb00000 {
compatible = "snps,dwc2";
reg = <0xffb00000 0xffff>;
interrupts = <0 125 4>;
clocks = <&usb_mp_clk>;
clock-names = "otg";
phys = <&usbphy0>;
phy-names = "usb2-phy";
status = "disabled";
};
usb1: usb@ffb40000 {
compatible = "snps,dwc2";
reg = <0xffb40000 0xffff>;
interrupts = <0 128 4>;
clocks = <&usb_mp_clk>;
clock-names = "otg";
phys = <&usbphy0>;
phy-names = "usb2-phy";
status = "disabled";
}; CONTINUED...

## Slide 76: socfpga.dtsi (28/28)
watchdog0: watchdog@ffd02000 {
compatible = "snps,dw-wdt";
reg = <0xffd02000 0x1000>;
interrupts = <0 171 4>;
clocks = <&osc1>;
status = "disabled";
};
watchdog1: watchdog@ffd03000 {
compatible = "snps,dw-wdt";
reg = <0xffd03000 0x1000>;
interrupts = <0 172 4>;
clocks = <&osc1>;
status = "disabled";
};
sysmgr: sysmgr@ffd08000 {
compatible = "altr,sys-mgr", "syscon";
reg = <0xffd08000 0x4000>;
};
};
};

## Slide 77: skeleton.dtsi
/*
* Skeleton device tree; the bare minimum needed to boot; just include and
* add a compatible value. The bootloader will typically populate the memory
* node.
*/
/ {
#address-cells = <1>;
#size-cells = <1>;
chosen { };
aliases { };
memory { device_type = "memory"; reg = <0 0>; };
};

## Slide 78: Thank you